# Trace Tables

## Perform Trace Tables on the following:

|  | Pseudocode (underneath each one describe what it does) | Trace Table (create a table with a column for each variable in the algorithm and one for the output, it is handy to include the conditions, too. Some tables have been started for you…) |
| --- | --- | --- |
| 1. | BEGIN READ pages IF pages<2000 THEN cost ( 0.3 x pages+100 ELSE cost ( 0.35 xpages+150 ENDIF DISPLAY cost END Use data 2500, 1000 and 2000 in separate Trace Tables | test# pages <2000? cost output 1 2 3 2500 1000 2000 F T F .35x2500+150=975 .3x1000+100=400 .35x2000+150=850 1025 400 850 This algorithm…calculates the cost of printing a large print run |
| 2. | BEGIN READ weight IF weight >= 2 THEN IF weight < THEN postage ( 4.5 ELSE postage ( 6.75 ENDIF ELSE postage ( 2.65 ENDIF total ( postage x weight DISPLAY total END Use data 7, 5, 3, 2, 1 in separate Trace Tables | test# weight >=2? <5? postage total output 1 2 3 4 5 7 5 3 2 1 T T T T F F F T T - 6.75 6.75 4.50 4.50 2.65 47.25 33.50 4.5*3=13.5 4.5*2=9 2.65*1=2.65 47.25 33.50 13.50 9.00 2.65 This algorithm…calculates the postage rate based on weight and calculates and displays the total cost |
| 3. | BEGIN total ( 0 FOR count ( 1 TO 7 DO READ score total ( total + score ENDFOR average ( total/count DISPLAY total, average END Use data 78, 22, 45, 60,100, 85, 58 | Note the order of these matches the order in the loop – makes it easier! count score total average output 1 2 3 4 5 6 7 78 22 45 60 100 85 58 0 78 100 145 205 305 390 448 448/7=64 64 This algorithm…calculates the total and average of 7 scores |
| 4. | BEGIN FOR inch ( 1 TO 12 DO DISPLAY inch, 2.54*inch END FOR END | inch output 1 2 3 4 5 6 7 8 9 10 11 12 1 2.54 2 5.08 3 7.62 4 10.16 5 12.70 6 15.24 7 17.78 8 20.32 9 22.86 10 25.40 11 27.94 12 30.48 This algorithm…converts inches to cm and displays it as a conversion table. |
| 5. | BEGIN READ temp m_temp ( temp FOR time ( 2 TO 12 DO READ temp IF temp > m_temp THEN m_temp ( temp ENDIF ENDFOR DISPLAY m_temp END Use data 33, 26, 35, 28, 34, 40, 15, 32, 23, 44, 55, 42 | time temp >m_temp? m_temp output 2 3 4 5 6 7 8 9 10 11 12 33 26 35 28 34 40 15 32 33 44 55 42 F T F F T F F F T T F 33 33 35 “ “ 40 “ “ “ 44 55 55 55 This algorithm…finds the maximum in a list of 12 values and displays it |
| 6. | BEGIN num ( 10 c_ford ( 0 FOR count ( 1 TO num DO READ model IF model = “FORD” THEN c_ford ( c_ford+1 ENDIF ENDFOR n_ford ( num – c_ford DISPLAY c_ford, n_ford, num END Use data FORD, NISSAN, FORD, FORD, HOLDEN, HOLDEN, MAZDA, MAZDA, FORD, HOLDEN | num count model =”FORD”? c_ford n_ford output 10 1 2 3 4 5 6 7 8 9 10 FORD NISSAN FORD FORD HOLDEN HOLDEN MAZDA MAZDA FORD HOLDEN T F T T F F F F T F 0 1 “ 2 3 “ “ “ “ 4 “ 10-4=6 4,6,10 This algorithm…counts the number of Fords in 10 cars and displays the number of Fords, non-Fords and total |