## Slide 1: Computer Architecture
What components are used
How are they related
Notes: Concepts
In general system terms ‘architecture’ specifies the components that make up a system and their relationship to each other.
Architecture can refer to different levels in an information system; for example architecture of a CPU, architecture of a computer system as a whole, architecture of a network, architecture of an OS
Hence ‘relationship’ does not necessarily refer just to how the components are interconnected, but may instead (or as well as) refer to how they interact with each other.
This presentation looks in very general terms at two levels of architecture: the CPU, and the Computer System.
Note: it does not look at how the components actually work or at what their role in a system is. It is assumed that students have seen this before, or will have it explained to them by the teacher
In class
Display main heading: ask students “what is computer architecture?”
Click to reveal first point, then ask “but is it just about what components make up the computer?”
Click to reveal second point.
Explain.
Student notes
Heading and definition (the more formal definition may be dictated if desired)

## Slide 2: Architecture – the CPU
Intola
32000
Control Unit
- instruction set
ALU
Registers
Internal buses
Cache (level 1)
Pipelines
Virtual memory support
Floating Point Unit
Clock
Speed
(Hz)
Internal
Bus size
8-bit
16-bit
32-bit
64-bit
128-bit…
Notes: Concepts
Functionally, the components of the microprocessor or CPU are (at least)
a control unit – this is effectively where the instruction set resides
an ALU
one or more registers for holding working data
one or more internal buses
It could also have
cache (often called level 1 cache)
one or more pipelines
virtual memory support (an OS function but hardware can help)
floating point unit
and lots more …
Two other specifications of importance
the clock speed
the internal bus width
In class
Explain: “First we will look at the Central Processing Unit
…these days it’s a single plastic or ceramic package with lots of pins coming out of it
…What’s inside the package?
Click and explain: “A ‘chip’ – a wafer of silicon crystal that has microcircuitry etched upon it (equivalent to perhaps millions of transistors)”
Ask: what kind of components would be on this ‘chip’?
Click each and explain/remind what each is. Note difference between ‘must haves’ (black) and ‘can haves’ (blue)
Ask: “There are two other important specifications that can be considered as part of a computers architecture. Can you guess what they are?”
Click to reveal Clock Speed – explain/remind
Then click to reveal Internal Bus Size – explain/remind (Note: this is the bus size inside the actual chip and that may be different from the bus the chip presents to the outside world)
Student Notes
Heading plus component lists

## Slide 3: Architecture – the Computer System
Virtual Memory
SCSI
USB
Control
DMA
controller
Cache
(level 2)
Main
Memory
(ROM & RAM)
I/O
Controllers
& Interfaces
Data bus
Address bus
Intola
32000
Notes: Concepts
This is one way of interconnecting components at this level of architecture
It shows the main components of an ‘ordinary’ system.
Not all these components are ‘must haves’, but a basic system has to at least have:
a microprocessor
a data bus
an address bus
memory (ROM and RAM)
a facility for getting data into and out of the system
From a design point of view:
the I/O and storage devices shown are those an ‘ordinary’ system would have, but none are necessary.
virtual memory, Cache, DMA. and other buses (eg USB) are all optional
It all depends on what you want out of a system.
Also, some CPUs provide a separate I/O bus
In class
Explain: “Now lets ‘zoom out’ and place the CPU inside a computer system.
… It is now just a component in a larger system whose architecture we now look at in general terms.
Ask: “How does the CPU get data to other parts of the system?”
Click to reveal ‘data bus’
Ask: “How does the CPU tell other parts of the system where the data has to go
Click to reveal ‘address bus’
Ask: “When we run a program, where is it stored?”
Click to reveal ‘main memory’
Ask: “How do we get data into and out of the system?”
Click to reveal ‘i/o controllers’. Give examples such as video card, sound card, NIC, … and explain/remind their function.
Ask: “what other features could we have on our computers to enhance performance and/or usability?”
Click to reveal: cache, virtual memory, dma, use, scsi
Student notes
Students could draw and label a block diagram based on completed slide, indicating ‘must haves’ for a basic system.

## Slide 4
Impact of … | on CPU performance | on overall system performance
Clock speed
Instruction set
Internal CPU bus width
Cache
Pipelines
Floating Point Unit
External bus width
External bus bandwidth
Virtual memory
DMA
Notes: NOTE: may have to fiddle with text colours here if no good on your projector!
Concepts
A system’s architecture determines its performance:
components are important; eg the type of processor
but so is how they are interconnected; eg ‘bottlenecks’
For the table:
Clock speed higher clock frequency -> faster execution of instructions -> should lead to faster overall performance
Instruction set can affect overall ‘speed’ of processor (efficiency of execution of software), but can only be changed by buying a different processor; eg Intel (IBM compatible) versus Motorola (Apple)
Internal CPU bus width depends on data and instructions being processed, but generally the wider the bus, the faster the internal data transfer should be, hence the faster processing should be -> faster overall performance
Cache depends on type of activity processor is engaged in; if lots of memory operations are being performed (as opposed to lots of arithmetic activity), then speed of processing should improve -> overall system performance should improve
Pipelines should make for faster execution of instructions -> should lead to faster overall performance
Floating Point Unit depends on type of activity processor is engaged in; if lots of arithmetic activity, then speed of processing will improve -> overall system performance should improve
External bus width will not impact on processor; in general the wider the bus the better the system performance should be, but it will depend on components connected to it
External bus bandwidth will not impact on processor; in general the higher the bandwidth the better the system performance should be, but it will depend on components connected to it (remember ‘bandwidth is a measure of capacity, not performance)
Virtual memory will not impact on processor; will improve system performance in the sense that larger programs can be run, but will slow down overall system speed. Generally, the greater its use, the slower the overall system will operate
DMA will indirectly impact on processor by freeing it up to do other things while a disk-to/from-memory data transfer (or similar) takes place; should improve overall system performance.
There are lots of ‘shoulds’ at the overall system level because, for example, while increasing clock speed will increase the speed of the processor, this is not guaranteed to improve overall system performance; if, for example, memory is small, the processor may be executing instructions at a blinding speed, but it is waiting eons for data to come in from disk.
In class
Explain:
Why are we interested in this? We are not going to design a computer system, let alone a microprocessor!
No, perhaps not, but you may have to choose a computer that has to meet certain performance criteria; eg
highend, desktop workstation for doing graphics work
fileserver for 150 workstations
dedicated print server
and so on.
Different applications require different levels of performance in different areas; eg
graphics – processor with a floating point unit will be or great benefit
fileserver – floating point unit will not enhance performance in this application
And these options all change the price of the system. So, if money is to be spent wisely, some knowledge of what the components are is useful.
Click to show table contents one at a time.
As each item comes up, use it as an opportunity to refresh memories about what they are.
Ask what goes in the two columns for that item (see above – may have to paraphrase)
Student notes
Copy table and fill in